Zeid Al-Ameedi
Cpts 360 PreLab #1

Notes:

BSS = uninitialized data (global/static)
DATA = initialized global variables (or static)
TEXT = storage of executable instructions
EXE = simply the amount of bytes the file contains

Case	a.out	TEXT	DATA	BSS
(1)	7236	1507	304	8
(2)	7240	1507	308	4
(3)	7236	1507	304	40032
(4)	47260	1507	40328	4
(5)	7316	1710	308	8
(6)	7328	1523	304	40068

Questions
1) Based on the most recent source file:
  DATA will contain variables a, b, c (initialized global, static local vars)
  BSS will contain variable g, d (Uninitialized g/s vars)

2) An a.out file consists of a header (sizes), followed by code and data sections. Keep in mind symbol table is optional for debugging. What isn’t in the a.out is the BSS section. Only its size is recorded in the header. That’s because later on the bss section is cleared to 0, so all the uninitialized globals and static locals start with a value of 0.

3) Static linking observations:

Case	a.out	TEXT	DATA	BSS
(1)	661728	582058	11264	3344
(2)	661728	582058	11264	3344
(3)	661728	582058	11264	43344
(4)	701760	582058	51296	3344
(5)	661728	582106	11264	3344
(6)	661820	582074	11264	43376

3 Cont) The sizes within static linking are much larger than that of dynamic linking. This is because the C-libraries are included when we compile in static form. So that binary executable can now be run on any platform/machine because it contains all the libraries that it could possibly reference based on its version. Thus it’s a much bigger package.